## Slide 1
Class 3: Layered Protocol Architecture
Khaled Mahmud Shahriar
Assistant Professor, Dept. of CSE, BUET khaledshahriar@cse.buet.ac.bd
CSE 321 Computer Networks July 2018 Term

## Slide 2: Why Layering
A complex task is broken into subtasks: modular design
  Each subtask is implemented separately as a layer, arranged in a vertical stack
Each layer performs a related subset of the functions required to communicate with another system.
  It relies on the next lower layer to perform more primitive functions and to conceal the details of those functions.
  It provides services to the next higher layer.
  Layers should be defined so that changes in one layer do not require changes in other layers.
So, instead of using a single complex protocol, it’s more flexible to implement a stack of protocols!
  Reduce the design and development workload significantly!

## Slide 3: Protocol Hierarchies
Protocols are stacked vertically as series of ‘layers’.
Each layer offers services to layer above, shielding implementation details.
Layer n on one machine communicates with layer n on another machine (they are peer processes/entities) using Layer n Protocol.

## Slide 4: Protocol Hierarchies
Layers, protocols, and interfaces.

## Slide 5: Virtual & Actual Communications
Important to understand difference between:
  virtual and actual communications,
  protocols and interfaces.
Peer processes ‘think’ of communications as being ‘horizontal’ using protocol.
Actual communications is via interfaces (and the physical communications medium).
Peer process idea is key to network design.

## Slide 6: The Relationship of Services to Protocols
The relationship between a service and a protocol.

## Slide 7: Examples of Service
Addressing
Routing
Error control
Reliability
Flow Control
Multiplexing
Fault tolerance
Scalability
Quality of service
Security

## Slide 8: Vertical Stack
Application A
Module A
Module T
Module I
Module N
Module P
Application B
Module B
Module C
Application C
Module W
can be replaced by other modules
Application developers
Operating System
Hardware

## Slide 9: TCP/IP protocol stack
application: supporting network applications
  FTP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.111 (WiFi), PPP
physical: bits “on the wire”

## Slide 10: ISO/OSI reference model
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine-specific conventions
session: synchronization, checkpointing, recovery of data exchange
Internet stack “missing” these layers!
  these services, if needed, must be implemented in application
  needed?

## Slide 11: OSI Model and TCP/IP Model Comparison
In the OSI model, the network access layer and the application layer of the TCP/IP model are further divided to describe discrete functions that must occur at these layers.
Notes: 3.2 – Network Protocols and Standards
3.2.4 – Reference Models
3.2.4.4 – OSI Model and TCP/IP Model Comparison

## Slide 12: TCP/IP Protocol Suite
Notes: 3.2 – Network Protocols and Standards
3.2.2 – Protocol Suites
3.2.2.3 –TCP/IP Protocol Suite

## Slide 13: Example: File Transfer
Host A
Router
Host B

## Slide 14: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame

## Slide 15: Encapsulation in the TCP/IP Suite

## Slide 16: Example: Web Browsing
Application Layer
Transport Layer
Internet Layer
Network Layer
Physical Network
Application Layer
Transport Layer
Internet Layer
Network Layer
HTTP Message
TCP Packet
Ethernet
Frame
Ethernet
Frame
IP Datagram
IP Datagram
Internet Layer
Network Layer
Physical Network
Host B
Host A
Router

## Slide 17
Thank You